## Slide 1: Core Facility at CEITEC BUT
David Škoda
CEITEC BUT
Brno, 10 June 2013

## Slide 2: CORE FACILITY “definition”
Core facilities can be defined as
centralized shared resources
that provide access to instruments, technologies, services, as well as expert consultation and other services to scientific investigators.
The typical core facility is a discrete unit with in an institution and has dedicated personnel, equipment, and space for operations.

## Slide 3: … in scientific meaning
scientist

## Slide 4: … in scientific meaning
scientist
infrastructure of CEITEC core facilities

## Slide 5: … in scientific meaning
scientist
equipped laboratories

## Slide 6: … in scientific meaning
25/8/367 of laboratory work
scientist

## Slide 7: … in scientific meaning
scientist
Result - publication, cooperation,
fundamental and application research

## Slide 8
CORE FACILITY at CEITEC
CEITEC BUT

## Slide 9: Background of CORE FACILITIES at CEITEC BUT
vision of research CEITEC BUT programme
  RP1: Advanced Nanotechnologies and Microtechnologies
  preparation, characterization and analysis of the properties of nanostructures (semiconductor nanostructures, magnetic and metallic nanostructures, nanotubes and nanofibers)
  RP2: Advanced Materials
  advanced methods of synthesis, preparing of advanced materials and multifunctional composites with polymeric, ceramic, silicate or metallic matrixes, characterization of their structures on various dimensional scales and quantifying structure-property-function relationships on the various structural levels

## Slide 10
CORE FACILITIES - construction site
April 2012
CFs

## Slide 11
CORE FACILITIES - construction site
April 2012 -> April 2013
CFs

## Slide 12
CORE FACILITIES - construction site
April 2012 -> April 2013 -> August 2014
CFs
CFs

## Slide 13
CORE FACILITIES - construction site
April 2012 -> April 2013 -> August 2014
CFs
CFs
  current situation:
  CFs under construction – no clean labs of sufficient areas
  RP1, RP2 - wide spectrum of interests
  continuous scientific work
  collaborations
  problem solution:
  purchasing a part of CF instruments + temporal installation (BUT, MU)
  sharing the instrument in established RG (RP1, RP2) laboratories
  cooperation with other institutions (universities, AS, CF)

## Slide 14
Key equipment of CFs at CEITEC BUT

## Slide 15: FIB/SEM – Tescan Lyra3 XMH

## Slide 16: FIB/SEM – Tescan Lyra3 XMH
FEG SEM
  U = 200 V – 30 kV
  I = 2 pA – 200 nA
  resolution < 1,2 nm with 30 kV
  detectors
    SE, BSE, TE
    In-beam SE a BSE
    EBIC
Focused Ion Beam - Ga Liquid Metal Ion Source
  U = 0,5 kV – 30 kV
  I = 1 pA – 40 nA
  resolution < 5nm with 30 kV
Gas Injection System
  5 precursors - Pt, W, SiO2, H2O, XEF2
4 nanomanipulators
EDX
installed at BUT, CLR
9
10

## Slide 17: FIB/SEM – Tescan Lyra3 XMH
selective Si etching (IBD, GIS)
Dynamic switching of the spin circulation …
V. Uhlíř, M. Urbánek, T. Šikola et al.
Nature Nanotechnology, Volume: 8 Issue: 5, 2013
magnetic nanodisks
fabrication (EBL, FIB )
10

## Slide 18: SNOM - Nanonics MultiView 4000
11

## Slide 19: SNOM - Nanonics MultiView 4000
odkaz na beziho
two-independent probe scanning system, sample scanning
SNOM, AFM, STM
combined SNOM collection, illumination with reflection and transmission modes
probes - sort of bent optical fibres
tuning fork according to applications
optical and acoustic hoods
Detectors:
  APD (VIS) + PMT (NIR)
Lasers:
  fiber coupler + bandpass filters
  Nd:YAG - 532 nm
  HeNe - 632,8 nm
2-probe SNOM system
installed at MU, CLR
11

## Slide 20: SNOM - Nanonics MultiView 4000
topography
SNOM
topography
SNOM
Control and Near-Field Detection …
P. Dvořák, T. Neuman, T. Šikola et al.
Nano Letters, May 2013
4-way evanescent
way interaction
binary sample

## Slide 21: FT – IR Bruker Vertex 80v + Hyperion 3000

## Slide 22: FT – IR Bruker Vertex 80v + Hyperion 3000
installed at MU
FT-IR – Vertex 80v
spectr. range 10 – 15 000 cm-1
detector 4 000-15 000 cm-1
reflection and transmission
IR microscope – Hyperion 3000
spectr. range 600 – 7 000 cm-1
detector 900-4 000 cm-1 (array)
up to 32x zoom (IR)
ATR
optical and acoustic hoods
13

## Slide 23: FT – IR Bruker Vertex 80v + Hyperion 3000
plasmonic antennas optimized for IR region
IR reflectance
13

## Slide 24: Spectroscopic ellipsometry NUV – FIR J. A. Woollam
installed at MU
unique instruments
components for newly built vacuum chamber
forming the RP1 objectives DEVELOPMENT OF NEW TECHNIQUES AND METHODS
12

## Slide 25: Spectroscopic ellipsometry NUV – FIR J. A. Woollam
installed at MU
Woollam IR-VASE
spectroscopic ellipsometer for mid infrared range
Fourier transform spectrometer, 1.7-3000 mm (300-7000 cm-1)
rotating compensator (CsI)
precise determination of D
determination of depolarization
Muller matrix
automated change of angle of incidence
Woollam VASE
two grating monochromator, 2500-190 nm
detectors InGaAs-Si + PMT
adjustable compensator (auto-retarder)
precise determination of D
determination of depolarization
Muller matrix
automated change of angle of incidence
12

## Slide 26: Tescan Mira3 - lithography SEM
14

## Slide 27: Tescan Mira3 - lithography SEM
FEG SEM – Tescan Mira3
  U = 200 V – 30 kV
  I = 2 pA – 200 nA
  resolution < 1,2 nm with 30 kV
  detectors
    SE, In-beam SE
interferometric stage - Raith
  resolution < 2 nm
  repeatability < 40 nm
  stitching field
lithographic software – Elphy Plus
  GDSII compatibility
installed at MU, CLR
14

## Slide 28: Diffractometer - Rigaku
11

## Slide 29: Booking system – monitoring the activities
web database of instruments

## Slide 30: CF projects
ongoing projects:
CF Open Access
  available and accessible for the external Czech and international research teams
  20 % of lab time to external academic users for free
  CEITEC instruments + shared instruments of RP1, RP2 group
  http://www.ceitec.eu/project-ceitec-open-access/t1368

## Slide 31: Thank you for your attention
Central European Institute of Technology
c/o Masaryk University
Žerotínovo nám. 9
601 77 Brno, Czech Republic
www.ceitec.eu | info@ceitec.cz

## Slide 32: recently installed - Lithography SEM
SEM objective
Electron Beam Lithography
star
concentric
circles
interferometric stage
14

## Slide 33: NTegra Spectra - SPM + mRaman -> TERS
15

## Slide 34: recently installed - SPM + mRaman -> TERS
installed at MU, CLR service
NTegra Spectra
SPM–
  AFM, STM, MFM, …
  cantilever, tuning fork
optical microscope –
  NUV-VIS-NIR
Raman spectrometer –
  EMCCD (VIS) + InGaAS (NIR)
  grat. 150 + 600 + 1800 gr/mm, Echelle
Lasers
  dual NUV/blue - 325nm + 441nm
  green solid state - 532nm
  NIR diode laser - 785nm
  supercontinuum - 400-1600 nm, for luminescence and excitations
Tip Enhanced Raman Spectroscopy capable
15

## Slide 35: recently installed SPM + mRaman -> TERS
SPM dock station
Spectra 3 – Raman spectrometer
Raman map of graphene flakes
15